## Slide 1
Chapter 2
Concepts & Technologies

## Slide 2: Outline
Concepts and enabling technologies of cloud computing
  Virtualization
  Load balancing
  Scalability & Elasticity
  Deployment
  Replication
  Monitoring
  MapReduce
  Identity and Access Management
  Service Level Agreements
  Billing
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 3: Virtualization
Virtualization refers to the partitioning the resources of a physical system (such as computing, storage, network and memory) into multiple virtual resources.
Key enabling technology of cloud computing that allow pooling of resources.
In cloud computing, resources are pooled to serve multiple users using multi-tenancy.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 4: Hypervisor
The virtualization layer consists of a hypervisor or a virtual machine monitor (VMM).
Hypervisor presents a virtual operating platform to a guest operating system (OS).
Type-1 Hypervisor
  Type-I or the native hypervisors run directly on the host hardware and control the hardware and monitor the guest operating systems.
Type-2 Hypervisor
  Type 2 hypervisors or hosted hypervisors run on top of a conventional (main/host) operating system and monitor the guest operating systems.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info
Type-1 Hypervisor
Type-2 Hypervisor

## Slide 5: Types of Virtualization
Full Virtualization
  In full virtualization, the virtualization layer completely decouples the guest OS from the underlying hardware. The guest OS requires no modification and is not aware that it is being virtualized. Full virtualization is enabled by direct execution of user requests and binary translation of OS requests.
Para-Virtualization
  In para-virtualization, the guest OS is modified to enable communication with the hypervisor to improve performance and efficiency. The guest OS kernel is modified to replace non-virtualizable instructions with hyper-calls that communicate directly with the virtualization layer hypervisor.
Hardware Virtualization
  Hardware assisted virtualization is enabled by hardware features such as Intel’s Virtualization Technology (VT-x) and AMD’s AMD-V. In hardware assisted virtualization, privileged and sensitive calls are set to automatically trap to the hypervisor. Thus, there is no need for either binary translation or para-virtualization.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 6: Load Balancing
Cloud computing resources can be scaled up on demand to meet the performance requirements of applications.
Load balancing distributes workloads across multiple servers to meet the application workloads.
The goals of load balancing techniques include:
  Achieve maximum utilization of resources
  Minimizing the response times
  Maximizing throughput
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 7: Load Balancing Algorithms
Round Robin load balancing
Weighted Round Robin load balancing
Low Latency load balancing
Least Connections load balancing
Priority load balancing
Overflow load balancing
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 8: Load Balancing - Persistence Approaches
Since load balancing can route successive requests from a user session to different servers, maintaining the state or the information of the session is important.
Persistence Approaches
  Sticky sessions
  Session Database
  Browser cookies
  URL re-writing
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 9: Scalability & Elasticity
Multi-tier applications such as e-Commerce, social networking, business-to-business, etc. can experience rapid changes in their traffic.
Capacity planning involves determining the right sizing of each tier of the deployment of an application in terms of the number of resources and the capacity of each resource.
Capacity planning may be for computing, storage, memory or network resources.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 10: Scaling Approaches
Vertical Scaling/Scaling up:
  Involves upgrading the hardware resources (adding additional computing, memory, storage or network resources).
Horizontal Scaling/Scaling out
  Involves addition of more resources of the same type.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 11: Deployment
Cloud application deployment design is an iterative process that involves:
  Deployment Design
    The variables in this step include the number of servers in each tier, computing, memory and storage capacities of severs, server interconnection, load balancing and replication strategies.
  Performance Evaluation
    To verify whether the application meets the performance requirements with the deployment.
    Involves monitoring the workload on the application and measuring various workload parameters such as response time and throughput.
    Utilization of servers (CPU, memory, disk, I/O, etc.) in each tier is also monitored.
  Deployment Refinement
    Various alternatives can exist in this step such as vertical scaling (or scaling up), horizontal scaling (or scaling out), alternative server interconnections, alternative load balancing and replication strategies, for instance.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 12: Replication
Replication is used to create and maintain multiple copies of the data in the cloud.
Cloud enables rapid implementation of replication solutions for disaster recovery for organizations.
With cloud-based data replication organizations can plan for disaster recovery without making any capital expenditures on purchasing, configuring and managing secondary site locations.
Types:
  Array-based Replication
  Network-based Replication
  Host-based Replication
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info
Array-based Replication

## Slide 13: Monitoring
Monitoring services allow cloud users to collect and analyze the data on various monitoring metrics.
A monitoring service collects data on various system and application metrics from the cloud computing instances.
Monitoring of cloud resources is important because it allows the users to keep track of the health of applications and services deployed in the cloud.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info
Type | Metrics
CPU | CPU-Usage, CPU-Idle
Disk | Disk-Usage, Bytes/sec (read/write), Operations/sec
Memory | Memory-Used, Memory-Free, Page-Cache
Interface | Packets/sec (incoming/outgoing), Octets/sec(incoming/outgoing)
Examples of Monitoring Metrics

## Slide 14: Software Deﬁned Networking
Software-Defined Networking (SDN) is a networking architecture that separates the control plane from the data plane and centralizes the network controller.
Conventional network architecture
  The control plane and data plane are coupled. Control plane is the part of the network that carries the signaling and routing message traffic while the data plane is the part of the network that carries the payload data traffic.
SDN Architecture
  The control and data planes are decoupled and the network controller is centralized.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 15: SDN - Key Elements
Centralized Network Controller
  With decoupled the control and data planes and centralized network controller, the network administrators can rapidly configure the network.
Programmable Open APIs
  SDN architecture supports programmable open APIs for interface between the SDN application and control layers (Northbound interface). These open APIs that allow implementing various network services such as routing, quality of service (QoS), access control, etc.
Standard Communication Interface (OpenFlow)
  SDN architecture uses a standard communication interface between the control and infrastructure layers (Southbound interface). OpenFlow, which is defined by the Open Networking Foundation (ONF) is the broadly accepted SDN protocol for the Southbound interface.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 16: OpenFlow
OpenFlow is the broadly accepted SDN protocol for the Southbound interface.
With OpenFlow, the forwarding plane of the network devices can be directly accessed and manipulated.
OpenFlow uses the concept of flows to identify network traffic based on pre-defined match rules.
Flows can be programmed statically or dynamically by the SDN control software.
OpenFlow protocol is implemented on both sides of the interface between the controller and the network devices.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info
OpenFlow switch comprising of one or more flow tables and a group table, which perform packet lookups and forwarding, and OpenFlow channel to an external controller.

## Slide 17: Network Function Virtualization
Network Function Virtualization (NFV) is a technology that leverages virtualization to consolidate the heterogeneous network devices onto industry standard high volume servers, switches and storage.
Relationship to SDN
  NFV is complementary to SDN as NFV can provide the infrastructure on which SDN can run.
  NFV and SDN are mutually beneficial to each other but not dependent.
  Network functions can be virtualized without SDN, similarly, SDN can run without NFV.
NFV comprises of network functions implemented in software that run on virtualized resources in the cloud.
NFV enables a separation the network functions which are implemented in software from the underlying hardware.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 18: NFV Architecture
Key elements of the NFV architecture are
  Virtualized Network Function (VNF): VNF is a software implementation of a network function which is capable of running over the NFV Infrastructure (NFVI).
  NFV Infrastructure (NFVI): NFVI includes compute, network and storage resources that are virtualized.
  NFV Management and Orchestration: NFV Management and Orchestration focuses on all virtualization-specific management tasks and covers the orchestration and lifecycle management of physical and/or software resources that support the infrastructure virtualization, and the lifecycle management of VNFs.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 19: MapReduce
MapReduce is a parallel data processing model for processing and analysis of massive scale data.
MapReduce phases:
  Map Phase: In the Map phase, data is read from a distributed file system, partitioned among a set of computing nodes in the cluster, and sent to the nodes as a set of key-value pairs.
  The Map tasks process the input records independently of each other and produce intermediate results as key-value pairs.
  The intermediate results are stored on the local disk of the node running the Map task.
  Reduce Phase: When all the Map tasks are completed, the Reduce phase begins in which the intermediate data with the same key is aggregated.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 20: Identity and Access Management
Identity and Access Management (IDAM) for cloud describes the authentication and authorization of users to provide secure access to cloud resources.
Organizations with multiple users can use IDAM services provided by the cloud service provider for management of user identifiers and user permissions.
IDAM services allow organizations to centrally manage users, access permissions, security credentials and access keys.
Organizations can enable role-based access control to cloud resources and applications using the IDAM services.
IDAM services allow creation of user groups where all the users in a group have the same access permissions.
Identity and Access Management is enabled by a number of technologies such as OpenAuth, Role-based Access Control (RBAC), Digital Identities, Security Tokens, Identity Providers, etc.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 21: Billing
Cloud service providers offer a number of billing models described as follows:
Elastic Pricing
  In elastic pricing or pay-as-you-use pricing model, the customers are charged based on the usage of cloud resources.
Fixed Pricing
  In fixed pricing models, customers are charged a fixed amount per month for the cloud resources.
Spot Pricing
  Spot pricing models offer variable pricing for cloud resources which is driven by market demand.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info

## Slide 22: Further Reading
Network Functions Virtualization, http://www.etsi.org/technologies-clusters/technologies/nfv, Retrieved 2013.
OpenFlow Switch Specification, https://www.opennetworking.org, Retrieved 2013.
J. Dean, S. Ghemawat, MapReduce: Simplified Data Processing on Large Clusters, OSDI 2004.
VMware, Understanding Full Virtualization, Paravirtualization, and Hardware Assist, 2007.
Bahga & Madisetti, © 2014
Book website: www.cloudcomputingbook.info